## Slide 1: Spacecraft Design
Lunar INterconnection Keepers
Albéric de Lajarte

## Slide 2: Presentation
Introduction
Mission overview
System overview
Conclusion
Q/A

## Slide 3: Introduction
New emergence of interest for the Moon
  NASA Artemis program
  ESA HERACLES lander
  Private companies
The goal is to go beyond exploration
  Lunar base installation
  Lunar gateway
  Resources exploitation
  We need more infrastructure
HERACLES liftoff. Credits: ESA

## Slide 4: Mission overview
Create a network of satellite around the Moon to support lunar mission
  Low altitude polar orbit relay satellite
  L2 Halo orbit relay satellite
  Many mores possible …
Test new generation of electric engines
  For Moon-Earth transfer
  For Moon orbit station keeping
  For end of life
Notes: ESA mission

## Slide 5: Mission overview - Transfer
Constraints
  Minimize maneuvers
  Reduce exposition to radiation
  Minimize time travel
Solution
  Initial circular orbit at 15’000 km altitude
  Transfer to highly elliptical orbit with apogee at 347’000km altitude
  Cruising on stable manifold
  Stabilize to Halo orbit
Orbital parameter | Value
Semi-major axis | 21371 km
Eccentricity | 0
Inclination | 28.7°
RAAN | 0°
Argument of perigee | 230°
True anomaly | 270°
Period | 8:38h
Phase | DeltaV [m/s] | Duration
MEO insertion | 0 | 3:50h
Manifold insertion | 1207 | 4 years
Cruising | 50 | 60 days
Halo insertion | 0 | -
Station keeping | 518 | 5 years
End of life | 125 | 7 days
Total | 1900 | 9.2 years
Notes: SOYUZ launch vehicle
Avoid Van Allen 1st bet

## Slide 6: Mission overview - Transfer
Initial orbit
Transfer orbit
Manifold
Halo orbit
Trajectory simulation using GMAT simulator

## Slide 7: Mission overview – Final orbit
Far side relay
  Continuously relay data between the far side of the Moon and the Earth
Satellite Network
  Relay data between the poles and the Earth
  Work with polar orbiter
  More efficient with more satellite

## Slide 8: System overview
System engineering
Telecommunication
Propulsion
Electrical power
ADCS
Structure

## Slide 9: System overview - System engineering
Functional Analysis

## Slide 10: System overview - System engineering
Functional Analysis - Telecommunication

## Slide 11: System overview - System engineering
Functional Analysis - Propulsion

## Slide 12: System overview - System engineering
Functional Analysis – Electrical power

## Slide 13: System overview - System engineering
Functional Analysis - ADCS

## Slide 14: System overview - System engineering
Functional Analysis - Structure

## Slide 15: System overview - System engineering
System diagram

## Slide 16: System overview - System engineering
Mass budget
System | Mass [kg]
Structure | 471.5
Propulsion | 430
Telecommunication | 386
Electrical Power | 1072.3
ADCS | 93.6
Total wet mass | 2453.5
Margin | + 811.5

## Slide 17: System overview - System engineering
Power budget
Phase | MEO insertion | Manifold insertion |  |  | Station keeping |  | 
Mode | Low power | Charge | Thrust | Low power | Relay | Thrust | Low power
Structure | 128,4 | 128,4 | 248,4 | 128,4 | 128,4 | 248,4 | 128,4
Propulsion | 23,4 | 23,4 | 16583,4 | 23,4 | 23,4 | 16583,4 | 23,4
Telecomm. | 21,6 | 21,6 | 21,6 | 21,6 | 7221,6 | 21,6 | 21,6
Elec. Power | 12 | 576 | 1032 | 12 | 576 | 1032 | 0
ADCS | 60 | 60 | 60 | 60 | 60 | 60 | 60
Power IN | 0 | 13’519 | 13’519 | 0,0 | 13’519 | 13’519 | 0,0
Total power [W] | -294,48 | 12’547.8 | -8’015.4 | -294,5 | 3’907.8 | -8’015.4 | -280,1
Duration [h] | 3,83 | 3,5 | 4,3 | 0,9 | 350,4 | 0,0 | 55,3
Battery level [%] | 97,39 | 100,0 | 20,2 | 19,6 | 100,0 | 100,0 | 64,2

## Slide 18: System overview - System engineering
Link budget
Link | L2/Earth [dB] |  | L2/Moon [dB] | 
Emitter | L2 | Earth | L2 | Earth
 | 59,4 | 128,0 | 65,6 | 55,3
Path | -224,6 | -224,6 | -208,1 | -208,1
Receiver | 50,8 | 32,4 | 38,6 | 38,6
SNR | 130,5 | 130,5 | 118,2 | 118,2
Margin | 16,1 | 66,4 | 14,2 | 3,9
Link | L2/Earth [dB] | 
Emitter | L2 | Earth
 | 14,0 | 117,0
Path | -212,5 | -213,0
Receiver | 37,5 | 6,0
SNR | 164,1 | 164,1
Margin | 3,1 | 74,1
Primary system
Secondary system

## Slide 19: System overview - System engineering
Data budget
System | Data rate [kbps]
Structure | 1.13
Propulsion | 23.06
Telecomm. | 0.56
Elec. Power | 3.93
ADCS | 24.56
Total with 30% contingency | 69.21

## Slide 20: System overview - Telecommunication
Goal
  Relay data between the Earth and the Moon
  Data rate between 1 and 100 Mbps
  Use once in Halo orbit
Solution
  Two parallel X band systems, one for the Earth, the other for the Moon
  Two high gain parabolic antenna
  ESTRACK network for the ground station
  BPSK with QPSK plus modulation, R-1/2 Viterbi decoding
Primary system
500 W X band transceiver from Advantech Wireless

## Slide 21: System overview - Telecommunication
Requirement
  Transmit internal data of the spacecraft
  Backup system for low power mode
  Constant link regardless of the attitude
Solution
  S band transceiver
  2 monopole antenna
  3.5 kbps data rate (5% of spacecraft’s data)
  ESTRACK network for the ground station
Secondary system
5W S band transceiver from Advantech Wireless

## Slide 22: System overview - Telecommunication
Block diagram

## Slide 23: System overview - Propulsion
Requirement
  Qualify new generation of ion thruster
  Used for the transfer to the Moon and the station keeping
  Used for desaturation of the CMG
Solution
  Two NEXT engine from Glenn Research Center and Aerojet Rocketdyne
  Engine mounted on a 2D gimbals
  Allow for thrust vectoring and differential thrust
Name | NEXT
Type | Ion engine
Isp | 4190 s
Thrust | 236 mN
Power | 6900 W
Efficiency | 70 %
Mass | 80.89 kg

## Slide 24: System overview - Propulsion
Block diagram

## Slide 25: System overview – Electrical Power
Requirements
  Power the thrusters
  Power the radio transceivers
  Manage eclipse phase
Solution
  2x6.8 kW Solar panels
  43.3 kWh Li-ion battery pack
  21 kW Power Conditioning Unit
PCU from Thales Alenia Space

## Slide 26: System overview – Electrical Power
Block diagram

## Slide 27: System overview – ADCS
Requirements
  Estimate and control the attitude of the spacecraft with 0.2° accuracy
  Estimate and control the orientation of the Solar panels with 10° accuracy
  Transfer 69 kbps of data inside the spacecraft
  Store one day of data
Solution
  Sensors: star tracker, sun sensor, accelerometer, gyros, GPS, magnetometer
  Actuator: 4 Control momentum Gyroscopes, 2 SADA
  Federated bus using the CAN protocol
  2 redundant 10 Go Flash memory

## Slide 28: System overview – ADCS
Block diagram

## Slide 29: System overview – Structure
Requirements
  Hold the systems together with a maximum acceleration of 4.3g
  Protect the spacecraft from thermal variation and overheating
  Protect the S/C from cosmic radiation
Solution
  Assembly of Honeycomb 76mm thick aluminum panels SF = 0.82
  Silver coated FEP surface + MIL for thermal protection
  Final dimensions of 1.4x1.4x3.1 meters (without Solar panels)

## Slide 30: System overview – Structure

## Slide 31: Conclusion
Overall Spacecraft successfully implemented
Very good learning opportunity
Transfer time not optimized enough
Collaboration with other lunar mission could have been better implemented

## Slide 32
THANK YOU FOR YOUR ATTENTION!
Discussion